## Slide 1: Gen4 -- Jetting Station SW Status
Slava Chuhovich
January 2014
Copyright © 2013 Stratasys Ltd. All rights reserved.
Company Confidential

## Slide 2: Ready for integration
Copyright © 2013 Stratasys Ltd. All rights reserved.
Company Confidential
Tester application (high level)
  User interface: complete redesign according to Meir’s requirements.
  Basic functionality, based on existing tester.
  New requirements: data arrangement, strobe, double pulse builder, etc...
  Communication with OHDB2 and OCB2 boards. New messages and registers.
  Voltage calibration algorithm.
  Operation for 16 cartridge lines: pumps, RFID, in-place sensors and load cells.
  Material level 12 thermistors reading and calibration.

## Slide 3: Ready for integration
Copyright © 2013 Stratasys Ltd. All rights reserved.
Company Confidential
OHDB2 MCU firmware
  New FPGA registers and head driver card logic.
  Temperature “ramp-up” control.
  Support 12 block filling thermistors, and their operation logic.
  Switching between head halves for voltage calibration.
  Adapting digital potentiometer operation for each head halve.
  Reading additional card voltages and reporting them to PC.
  Communication with PC. New messages and registers.

## Slide 4: Ready for integration
Copyright © 2013 Stratasys Ltd. All rights reserved.
Company Confidential
OCB2 MCU firmware
  Separate I2C driver and MSC Interface implementation.
  Support for “n” number of MSC cards. Implementing 16 pumps activation and logic, including actuators and sensors.
  Implement new “filling monitoring” for new block configuration (12 thermistors and their operation modes).
  New messages for PC communication.
  Additional code refactoring, small improvements and bug fixes.

## Slide 5: Performed testing
Copyright © 2013 Stratasys Ltd. All rights reserved.
Company Confidential
Tested against hardware simulator.
Tested and verified against actual OHDB2 and OCB2 cards with 4 MSC cards.
Correct signals were verified with Eldad using scope and SPI sniffer .

## Slide 6: Gaps
Copyright © 2013 Stratasys Ltd. All rights reserved.
Company Confidential
Very little SW testing was performed using actual head driver card with actual Gen4 heads. Most of the testing was done with OHDB2 card using E1 heads and electronics.

## Slide 7
Thank You
Copyright © 2013 Stratasys Ltd. All rights reserved.
Company Confidential